SECTION 10 8200

GRILLES AND SCREENS

PART 1  GENERAL

1.01	SECTION INCLUDES

A.	Aluminum grilles or Screen Applications attached to structure as indicated on the contract drawings.

1.02	RELATED REQUIREMENTS

A.	Section 03 3000 - Cast-in-Place Concrete:  Mounting substrates.

B.	Section 04 2000 - Unit Masonry:  Mounting substrates.

C.	Section 05 1200 - Structural Steel Framing:  Mounting substrates.

D.	Section 07 4213 - Metal Wall Panels:  Mounting substrates.

E.	Section 08 4313 - Aluminum-Framed Storefronts:   Mounting substrates.

F.	Section 08 4413 - Glazed Aluminum Curtain Walls:  Mounting substrates.

1.03	REFERENCE STANDARDS

A.	AAMA 611 - Voluntary Specification for Anodized Architectural Aluminum; 2012.

B.	AAMA 612 - Voluntary Specification, Performance Requirements, and Test Procedures for Combined Coatings of Anodic Oxide and Transparent Organic Coatings on Architectural Aluminum; 2015.

C.	AAMA 2605 - Voluntary Specification, Performance Requirements and Test Procedures for Superior Performing Organic Coatings on Aluminum Extrusions and Panels; 2013.

D.	ASTM A307 - Standard Specification for Carbon Steel Bolts, Studs, and Threaded Rod 60 000 PSI Tensile Strength; 2014.

E.	ASTM B209 - Standard Specification for Aluminum and Aluminum-Alloy Sheet and Plate; 2014.

F.	ASTM B221 - Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Profiles, and Tubes; 2014.

G.	ASTM B221M - Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Profiles, and Tubes [Metric]; 2013.

H.	ASTM D1187/D1187M - Standard Specification for Asphalt-Base Emulsions for Use as Protective Coatings for Metal; 1997 (Reapproved 2011).

I.	ASTM F593 - Standard Specification for Stainless Steel Bolts, Hex Cap Screws, and Studs; 2013a.

1.04	SUBMITTALS

A.	See Section 01 3000 - Administrative Requirements, for submittal procedures.

B.	Shop Drawings:  Submit detailed shop drawings, indicating component profiles, sections, finishes, fastening details, special details, and manufacturer's technical and descriptive data.

1.	Include field dimensions of openings and elevations on shop drawings.

2.	Indicate distinction between factory-assembled and field-assembled work on shop drawings.

C.	Samples:  Submit samples for color verification, 10 inches (254 mm) by 10 inches (254 mm) minimum.

D.	Samples:  Submit assembled sample 24 inches by 24 inches (610 mm by 610 mm) minimum size to illustrate design, fabrication techniques, workmanship and finish color.

E.	Delegated Design Data:  Submit comprehensive structural analysis of design for the specified loads. Stamped and signed calculations by professional engineer.

F.	Designer's Qualification Statement.

G.	Manufacturer's Qualification Statement.

H.	Warranty Documentation:  Submit manufacturer warranty and ensure that forms have been completed in Owner's name and registered with manufacturer.

1.05	QUALITY ASSURANCE

A.	Designer Qualifications:  Perform design under direct supervision of a Professional Engineer experienced in design of this type of work and licensed in the State in which the Project is located.

B.	Manufacturer Qualifications:  Company specializing in manufacturing products specified in this section, with not less than five years of documented experience.

C.	Installer Qualifications:  Company specializing in performing work of the type specified and with minimum three years of documented experience.

1.06	DELIVERY, STORAGE, AND HANDLING

A.	Deliver materials to project site in manufacturer's original, unopened packaging, with labels clearly identifying manufacturer and material.

1.07	WARRANTY

A.	See Section 01 7800 - Closeout Submittals, for additional warranty requirements.

B.	Correct defective work within a one year period after Date of Substantial Completion.

C.	Finish Warranty:  Provide manufacturer's ten year warranty on factory finish against cracking, peeling, and blistering.

PART 2  PRODUCTS

2.01	MANUFACTURERS

A.	Basis of Design: Metalwërks® (Screenwalls), (Grilles), (Custom Assemblies), or __________.

a. Substitutions:  See Section 01 6000 - Product Requirements.

2.02	ALUMINUM GRILLES

A.	Aluminum Grilles:  Provide shop fabricated, shop finished grilles assembled into panels. 	Choose:

1. Grille Type:  Tubular shape.

a.  Pattern:  as indicated on the contract drawings.

b.  Panel Depth:  _____ inch (_____ mm).

2  Screen Type:  Perforated metal sheet.

a. Hole Size and Spacing:  _____ inch (_____ mm) diameter, _____ inch 		     (_____ mm) apart.

b. Hole Shape:  __________.

c.	Panel Depth:  _____ inch (_____ mm) deep.

3. Extruded Aluminum: Blade Size and Configuration:  As indicated on drawings.

a.Custom Profile, Airfoil, and other geometric shaped blades will be provided in 	     sizes and lengths as shown on the Architectural Drawings.

b. Install internal stiffeners as required to support blades for span conditions 	      indicated.

c. Attachment clips, anchors and end-caps with weeps at each blade unit 		     where indicated.

4. Wire Mesh Infill Options:

a. Custom and standard aluminum or stainless steel patterns and wire weave 	    options

b.Opening areas: CHOOSE: opaque to 80% open areas – standard 1”, 1.5”, 2” 	    square options or Custom- (Consult Factory for available Options).

c. Mounting methods with integrated mullions: Inset or Outset styles

5.  Frame/Support:  Extruded aluminum tube or flat aluminum bar.

6. Wind Load Resistance:  Design to resist positive and negative wind load, ____ psf (____ kPa), without damage or permanent deformation.

2.03	MATERIALS

A.	Aluminum Extrusions:  ASTM B221 (ASTM B221M) alloy 6063, temper T5, 1/8 inch (3 mm)

minimum wall thickness.

B.	Aluminum Sheet:  ASTM B209 (ASTM B209M) alloy 5005, with temper as required for 	forming.

C.	Concealed Structural Supports:  Aluminum, Stainless Steel, or steel coated for corrosion 	resistance and dissimilar metal isolation.

2.04	FABRICATION

A.	Shop fabricate grilles to the greatest extent possible.

B.	Disassemble as necessary for shipping and handling, clearly mark units for proper 	reassembly.

C.	Provide supports, anchorages, and accessories as required for complete assembled system.

D.	Provide inserts as required for installation into concrete or masonry based support materials.

E.	Fabricate grilles to ensure proper fit into openings of sizes indicated, with tolerances for 	installation.

2.05	FINISHES

- Superior Performing Organic Top Coating:  Complying with AAMA 2605 for testing, performance, and application procedures, and consisting of Please Choose: [two-coat, three-coat, four coat] thermally cured polyvinylidene fluoride (PVDF) system.

- Class I Natural Anodized Finish:  AAMA 611  AA-M12C22A41 Clear anodic coating not less than 0.7 mils (0.018 mm) thick.

- Class I Color Anodized Finish:  AAMA 611  AA-M12C22A42 Integrally colored anodic coating not less than 0.7 mils (0.018 mm) thick.

- Finish Color:  As indicated on drawings.

- Finish Color:  As selected by Architect from manufacturer's standard range.

2.06   ACCESSORIES

A. Fasteners:  ASTM F593 stainless steel or ASTM A307 carbon steel, sizes to suit installation

conditions.

B.	Anchors and Inserts:  Corrosion resistant; type, size, and material required for loading and     	installation as indicated.

C.	Bituminous Paint:  Cold-applied asphalt emulsion complying with ASTM D1187/D1187M.

PART 3  EXECUTION

3.01	EXAMINATION

A.	Verify dimensions, tolerances, and method of attachment with other work.

B.	Verify that painting, roofing, masonry work, and other adjacent work that might damage grille 	finish has been completed prior to start of installation.

C.	Verify that anchorage devices have been properly installed and located.

3.02	INSTALLATION

A.	Install in accordance with manufacturer's written installation instructions.

B.	Coat concealed metal surfaces that will be in contact with cementitious materials or 	dissimilar metals with bituminous paint, and allow paint to dry prior to installation of aluminum 	components.

C.	Set grilles level, plumb, with uniform joints, and in alignment with adjacent work as indicated.

D.	Mechanically secure grilles to supporting structure.

E.	Do not cut or trim aluminum members without approval of manufacturer; do not install 	damaged members.

3.03	TOLERANCES

A.	Maximum Variation from True Position:  1/8 inch (3 mm).

B.	Maximum Offset from True Alignment:  1/8 inch (3 mm).

3.04	CLEANING

A.	Remove temporary protective covering as grilles are installed.

B.	Clean finished surfaces as recommended by manufacturer and maintain clean condition until 	Date of Substantial Completion.

C.	Touch-up damaged finish coating using material provided by manufacturer to match original          	coating.

D.	Replace grilles that have been damaged beyond touch-up repair.

3.05	PROTECTION

A.	Provide protection of installed grilles to ensure grilles are without damage until Date of 	Substantial Completion.

END OF SECTION